## Slide 1
WebFlux → Virtual Threads
Results from the three-machine AWS run
120 cells · 3 builds × 5 workloads × 4 rates × 2 repetitions
21 September 2026 · OpenJDK 25.0.4 · Spring Boot 4.1.1 · PostgreSQL 17 · k6 v2.2.0
Notes: These supersede the laptop numbers. One finding from that run is reversed here, and one could not be measured at all.

## Slide 2
TEST ARCHITECTURE
How the test machines were arranged
Load generator
k6
Offers a fixed rate whether
or not the system keeps up
Never the bottleneck
→
System under test
c7i.large · 2 vCPU · 4 GB
One build at a time on :8080
-Xmx1g, G1, pool of 20
The only thing measured
→
Backend
PostgreSQL 17 + stub
Database on its own CPUs
Stub returns after 200 ms
Never competes with the app
One availability zone
Cross-zone adds latency with real variance. Availability is irrelevant here; consistency is everything.
Only 2 vCPU under test
Deliberately small. A thread model only shows itself when something is scarce.
The system under test is a c7i.large: 2 vCPU, x86_64, 4 GB. Compute-optimised and non-burstable, so it cannot be throttled mid-run the way a t-family instance can. Its telemetry agrees independently — system_cpu_count reports 2, heap max 1 GB, OpenJDK 25.0.4 on Ubuntu, pool of 20 on both the JDBC and R2DBC sides.
Notes: CPU is the binding resource on this box, not memory: a 1 GB heap plus metaspace, code cache and thread stacks sits comfortably inside 4 GB even for the platform-thread build running ~290 threads. Nothing in the run was memory-constrained. The load generator and backend specs were not recorded; only the system under test is characterised here, which is the one that matters.

## Slide 3
WHAT WAS BUILT
Three builds, one variable each
webflux-r2dbc
Current stack. Netty, Spring Data R2DBC, r2dbc-postgresql, WebClient.
mvc-virtual
Candidate. Tomcat, Spring Data JDBC, JDBC driver, RestClient, virtual threads on.
mvc-platform
Reference. Byte-identical to mvc-virtual; virtual threads off.
mvc-virtual and mvc-platform share a byte-identical dependency list and controller, verified with diff. The entire difference between them is three lines of YAML, so any gap is the thread model and nothing else.

## Slide 4
WORKLOAD DESIGN
Five workloads, each isolating one constraint
Endpoint | Work | Conn. held | Latency | What constrains it
/nodb | Constant response | — | ~0.1 ms | nothing on this ladder
/db | One indexed query | < 1 ms | ~0.5 ms | nothing on this ladder
/db-heavy | Aggregate + 20 rows, padded | 11.96 ms | ~13 ms | pool, ~1,670 rps
/db-slow | Query + pg_sleep(0.1) | 101.8 ms | ~100 ms | pool, ~197 rps
/api | One 200 ms upstream call | — | ~200 ms | threads, ~1,000 rps
/api is the decisive workload. It touches no database, so nothing the connection pool does can explain what happens there — each request simply holds a thread for 200 ms.
Two knees moved from the figures the ladder was designed around. /db-heavy was planned at ~1,387 rps from a locally measured 14.4 ms hold; on AWS the hold is 11.96 ms, putting the knee at ~1,670 — which is where the data actually breaks. /db and /nodb never bind at any rate tested, so they serve as controls rather than measurements.

## Slide 5
METHOD
Sizing the experiment
Connection pool
ceiling = pool size / hold time
/db-heavy 20 / 0.012 s = 1,670 rps
/db-slow 20 / 0.102 s = 197 rps
/db 20 / 0.000x s = no limit
Requests in flight
in flight = rate x latency
/api 500 x 0.20 s = 100
/api 1,000 x 0.20 s = 200
/api 1,500 x 0.20 s = 300
Tomcat's default is 200 threads. That is why /api at 1,000 rps is the edge and the database workloads are not — they never put enough requests in flight for the thread model to matter.
Load was offered open-model at a fixed arrival rate, 60 s warmup discarded and 60 s measured. A closed-loop generator slows down when the system does, which hides the saturation behaviour being measured. One cell is one build at one workload at one rate: 3 × 5 × 4 = 60 cells, each run twice, 120 runs. The 15 runs where the generator could not sustain the rate are excluded.

## Slide 6
RESULTS
Latency: the two candidates are almost identical
Workload | Requests | WebFlux | Virtual threads | Platform threads
/nodb @ 2,000 rps | 120,000 | 0.1 ms | 0.1 ms | 0.1 ms
/db @ 2,000 rps | 120,000 | 0.5 ms | 0.5 ms | 0.4 ms
/db-heavy @ 1,000 rps | 60,000 | 12.7 ms | 12.4 ms | 12.4 ms
/api @ 500 rps | 30,000 | 200.9 ms | 200.9 ms | 200.9 ms
/api @ 1,000 rps | 60,000 | 200.6 ms | 200.6 ms | 668.0 ms
/api @ 1,500 rps | 90,000 | 200.5 ms | 200.6 ms | 1,000 ms · 100 %
/api @ 2,000 rps | 120,000 | 200.5 ms | 200.6 ms | 709.7 ms · 100 %
Median p50 of two repetitions. Requests is the measured 60-second window, offered rate x 60. Where the error rate is high the figure is floored by the 1,000 ms client timeout, so it is a lower bound on how bad it was — read the error rate first.
WebFlux and virtual threads are within 0.1 ms of each other on every workload and every rate tested. Nothing in the latency data distinguishes them.

## Slide 7
RESULTS · /API
/API - The thread ceiling
Chart: Median response time (ms) by offered rate
| 500 rps · 30k req | 1,000 rps · 60k req | 1,500 rps · 90k req | 2,000 rps · 120k req
WebFlux | 200.9 | 200.6 | 200.5 | 200.5
Virtual threads | 200.9 | 200.6 | 200.6 | 200.6
Platform threads | 200.9 | 668 | 1000 | 709.7
Platform threads: 0 % errors at 1,000 rps, 100 % at 1,500
At 1,000 rps the queue fills but does not overflow inside the one-second timeout — a p50 of 668 ms with every request still succeeding. At 1,500 it overflows and nothing gets through.
The application was never slow
At 1,500 rps the server completed 127,256 requests at a 202 ms mean and logged zero exceptions, while k6 recorded 100 % failure and time-blocked-before-sending reached 834 ms at p95. The requests were sitting in the accept queue, never reaching the application. 200 threads at 200 ms each caps throughput at 1,000 rps; the surplus simply accumulated.
At 1,500 rps that is all 90,000 requests failing, not a tail — platform threads returned nothing usable for a full minute.
Notes: The 2,000 rps platform-thread cell is marked invalid: the generator dropped iterations against an already-failing server, so its p50 of 709.7 ms understates the load.

## Slide 8
RESULTS · /DB-HEAVY
/DB-HEAVY - On the realistic database workload, reactive is the slower option
Chart: 95th percentile response time (ms) by offered rate
| 500 rps · 30k req | 1,000 rps · 60k req | 1,500 rps · 90k req
WebFlux | 13.4 | 15.9 | 313
Virtual threads | 13.1 | 12.8 | 19.7
Platform threads | 13.1 | 12.8 | 14.8
At 1,500 rps
 | p95 | p99 | cores
WebFlux | 313.0 | 409.3 | 0.613
Virtual threads | 19.7 | 33.2 | 0.233
Platform threads | 14.8 | 28.7 | 0.211
Reactive is roughly 16× slower at p95 here and uses 2.6× the CPU for the same query. At 2,000 rps it fails 58–61 % of requests and the generator can no longer sustain the rate; virtual threads fail 92 % but keep serving.
In absolute terms at 1,500 rps: of 90,000 requests, 4,500 were slower than 313 ms on reactive and 900 were slower than 409 ms. On virtual threads the same cuts fall at 19.7 ms and 33.2 ms. Nothing failed on either — this is entirely tail latency.

## Slide 9
RESULTS · /DB-HEAVY
Why the tail jumps to 313 ms
The delay is inside the application
the server's own timer, mean per request
500 rps 12.8 ms = the query itself
1,000 rps 16.4 ms
1,500 rps 65.7 ms 5x the query
What it is not
blocked p95 0.0 ms not the network
GC max pause 19 ms not collection
same DB, virtual 13.0 ms not the database
p50 unchanged 12.9 ms not everything
Every millisecond is in time-to-first-byte. Blocked, connecting and sending are all zero, so the request reached the server immediately. The server's own timer agrees: 65.7 ms on average to answer a 13 ms query. And it is bimodal - p50 stays at 12.9 ms while p95 reaches 313 ms, so most requests are untouched and about 4,500 of 90,000 wait roughly half a second.
Most likely cause: queueing on Netty's event loops. Reactor Netty runs a small fixed set of them - this app held 21 threads at every rate - shared between the HTTP server and the R2DBC driver. Decoding twenty rows costs 11 us each, and connections are pinned to a loop, so a request can wait behind several others on the same one. Raising reactor.netty.ioWorkerCount, or profiling the loop threads, would confirm it.

## Slide 10
RESULTS · /DB-HEAVY
In summary: reactive waits well, decodes expensively
Event-loop CPU per ms of request life
workload density p95
/api @ 2,000 0.09 % 201 ms
/db-heavy @ 1,500 3.17 % 313 ms
35x denser, 35x the loop pressure
Established by the data
cost is per row 11.2 vs 2.1 us
delay is in the app 65.7 ms server mean
not the DB, not GC, not the network
21 threads at every rate, no elasticity
/api spends 200 ms waiting on a socket, and waiting costs an event loop nothing - that is the model working exactly as designed, which is why reactive holds p50 at 200.5 ms from 500 all the way to 2,000 rps. /db-heavy hands the same loop a 408 us burst of row decoding and JSON serialisation per request, and a loop runs one task to completion before starting the next. Reactive is excellent where the work is waiting, and exposed where the work is CPU on the response path.
Not established: the size of the stall. Queueing arithmetic across four loops at roughly 15 % utilisation predicts sub-millisecond waits, not 313 ms, so something further is at work - most likely prefetch and backpressure inside r2dbc-postgresql, which this dataset cannot see.

## Slide 11
RESULTS · /DB-HEAVY @ 2,000 RPS
Where each stack chokes, and how differently
 | Errors | Client p50 | Server mean | Pool waiting | CPU
webflux-r2dbc | 61 % | 937 ms | 555 ms | 0 | 0.50
mvc-virtual | 92 % | 999 ms | 4,952 ms | 5,889 | 1.28
mvc-platform | 100 % | 1,000 ms | 124 ms | 175 | 0.41
The server-mean column is the one to read twice
Platform threads had the fastest application of the three — 124 ms per request — precisely because its 200-thread limit refused work it could not finish. Virtual threads removed that limit, admitted everything, queued 5,889 requests on a 20-connection pool and spent 4.9 seconds per request on work the client had already abandoned at one second.
Platform threads
Bounded admission
200 threads cap what enters. The queue forms outside the application, which stays healthy. Clients time out at the door.
Virtual threads
Unbounded admission
Nothing caps entry. Requests queue on the connection pool instead, and the application does seconds of work nobody is waiting for.
WebFlux
Cancellation propagates
When the client gives up, the reactive chain aborts the in-flight work. Least wasted effort of the three.
Notes: Both webflux cells and one mvc-virtual cell at this rate are marked invalid: the generator dropped iterations against an already-failing server, so their error rates understate the load. The mechanism each one shows is unaffected.

## Slide 12
RESULTS · ERROR CAUSES
What actually failed, and why
Workload · rate | Variant | Errors | Server 5xx | Waiting on pool | Cause
/api @ 1,500 | mvc-platform | 100 % | 0 | 0 | client timeout, accept queue
/db-heavy @ 2,000 | mvc-platform | 100 % | 0 | 175 | client timeout, accept queue
/db-heavy @ 2,000 | webflux-r2dbc | 61 % | 0 | 0 | client timeout, server too slow
/db-heavy @ 2,000 | mvc-virtual | 92 % | 17,399 | 5,889 | CannotGetJdbcConnectionException
/db-slow @ 1,500 | mvc-platform | 100 % | 0 | 179 | client timeout, accept queue
/db-slow @ 1,500 | webflux-r2dbc | 100 % | 165,159 | 0 | AbortedException
/db-slow @ 1,500 | mvc-virtual | 99 % | 80,170 | 7,826 | CannotGetJdbcConnectionException
Three signatures, consistent across every failing cell
mvc-platform
No server-side exception anywhere, ever. The application never saw the request. Pool waiting stays bounded at 0–179 because only 200 threads can be in flight.
mvc-virtual
CannotGetJdbcConnectionException — pool acquire timing out. Pool waiting reaches 4,294–7,826: admission is unbounded, so the queue moves to the database.
webflux-r2dbc
AbortedException and TransientDataAccessResourceException — the client disconnected and the reactive chain cancelled the work. Pool waiting is always 0.

## Slide 13
RESULTS
Resource use, and how it was measured
Workload · rate | WebFlux | Virtual threads | Platform threads
/nodb @ 2,000 | 0.119 | 0.123 | 0.123
/db @ 2,000 | 0.352 | 0.287 | 0.157
/db-heavy @ 1,500 | 0.613 | 0.233 | 0.211
/api @ 1,000 | 0.256 | 0.301 | 0.241
/api @ 2,000 | 0.356 | 0.560 | 0.326
Live threads | 21 | 20 – 79 | 215 – 288
CPU cores consumed per wall-second, median of two repetitions. The machine has 2, so 0.560 is 28 % of the box.
Reactive is cheapest where there is no database and most expensive where there is. On /api it uses 36 % less CPU than virtual threads; on /db-heavy it uses 2.6× more. Thread count is not a proxy for cost — platform threads run ten times as many as reactive while using less CPU than either.
Memory is the next slide. The heap gauge could not separate the builds — one sample per cell, 52–972 MB, because it sawtooths with GC — but allocation is a counter, and it separates them cleanly.

## Slide 14
MEMORY
Footprint is flat. Allocation is not.
Allocation per 1,000 requests | WebFlux | Virtual threads | Platform threads
/nodb @ 2,000 | 20 MB | 13 MB | 14 MB
/db @ 2,000 | 62 MB | 26 MB | 23 MB
/db-heavy @ 1,500 | 254 MB | 66 MB | 64 MB
/api @ 1,000 | 38 MB | 58 MB | 56 MB
/api @ 2,000 | 37 MB | 59 MB | —
Live set at overload | — | 801 MB | 187 MB
Megabytes allocated per 1,000 requests, median of two repetitions. A counter, so exact — unlike the heap gauge, which sawtooths.
The two builds differ in kind, not degree. Reactive allocates 3.8× more per request on /db-heavy — the same per-row decode cost that shows up as CPU — but that garbage dies young and G1 clears it in 0.43 s a minute. On /api the order reverses: reactive allocates 1.6× less, because waiting on a socket allocates nothing.
Live set is what is still reachable after an old-gen collection — not heap used, which also counts garbage. At /db-heavy 2,000 rps virtual threads retained 801 MB of 1,024 with 5,889 requests queued on 20 connections: 139 KB held per queued request, and 31.8 s paused in 124 s. Platform threads queue 175, capped by Tomcat — 187 MB. Virtual figure is one valid rep; WebFlux sustained neither.

## Slide 15
RESULTS · A CAVEAT
/db-slow measures the database, not the stacks
Every cell failed, in all three builds, at every rate. That is by construction, not a finding.
pg_sleep(0.1) -> 100 ms connection hold
ceiling = 20 connections / 0.1 s = 200 rps
lowest rate on the ladder = 500 rps (2.5x over)
And the ceiling falls as you push harder
Offered | Measured hold | Effective ceiling | Errors
500 rps | 101.8 ms | 197 rps | 99.1 %
1,000 rps | 127.6 ms | 157 rps | 99.0 %
1,500 rps | 151.4 ms | 132 rps | 98.9 %
2,000 rps | 160.5 ms | 125 rps | 99.4 %
pg_sleep is a fixed 100 ms, so the extra 60 ms is contention inside PostgreSQL once far more sessions are queued against it than the pool can serve. Overload makes the bottleneck narrower.
What this tells us, and what it does not
These numbers are a property of the pool size, the query duration, the database's CPU and its configuration — not of the three stacks. Change any one of those and the whole picture moves. A larger pool, a faster query or a bigger database would each shift the ceiling somewhere else entirely.
What it does show is how each stack behaves once it is past capacity, and they differ completely:
Platform threads
refuse work at the accept queue, 0.056 cores — almost idle
Virtual threads
admit it, exhaust the pool, 511k connection failures at 1.18 cores
WebFlux
admit it, 633k driver failures at 1.62 cores
Notes: If this workload is to say anything about the candidates, it needs its own ladder below the ceiling - 50 to 300 rps - or a pool sized for the rates being offered. As run, it is a demonstration of failure modes.

## Slide 16
MIGRATION
Ecosystem: what changes with the driver
 | WebFlux + R2DBC (today) | MVC + virtual threads
PostgreSQL driver | r2dbc-postgresql 1.1.2 | postgresql 42.7.13
Connection pool | R2DBC Pool | HikariCP
ORM | none available | Hibernate / Spring Data JPA
Query APIs | DatabaseClient | JdbcClient, JdbcTemplate, JPA
Transactions | reactive, context-bound | @Transactional, thread-bound
Migrations | Flyway needs a JDBC driver anyway | Flyway natively
Tracing context | Reactor Context, plumbed explicitly | ThreadLocal / MDC works
Stack traces | reactor internals | our own classes
A reactive service already ships a JDBC driver for schema migrations, so moving does not add a dependency there — it removes the second one.

## Slide 17
WHERE THIS LEAVES US
Virtual threads are a credible replacement. The open question is cost, not capability.
Capability
Matched WebFlux on latency at every rate on every workload tested, within 0.1 ms.
CPU
36 % more on /api, where there is no database. 2.6× less on /db-heavy, where there is. The direction depends on the workload.
Memory
Footprint did not separate the builds; allocation did. Reactive allocates 3.8× more per request on /db-heavy and 1.6× less on /api. Under overload virtual threads retain heap in proportion to what they admit — 801 MB of 1,024 at /db-heavy 2,000 rps.
Engineering
Ordinary code, real stack traces, working debuggers, a mature driver, a larger hiring pool.
Two repetitions per cell in a single session. Differences of the size seen on /db-heavy and /api are safe to act on; smaller ones are not.

## Slide 18
APPENDIX · ALL CELLS
/nodb — every cell
rate | build | valid | err % | p50 | p95 | p99 | cores | MB/1k | live MB
500 | webflux | 2/2 | 0.0 | 0.4 | 0.5 | 0.6 | 0.086 | 20 | 213
500 | virtual | 2/2 | 0.0 | 0.3 | 0.5 | 0.6 | 0.078 | 10 | 102
500 | platform | 2/2 | 0.0 | 0.3 | 0.5 | 0.6 | 0.083 | 18 | 121
1,000 | webflux | 2/2 | 0.0 | 0.2 | 0.4 | 0.6 | 0.099 | 20 | 213
1,000 | virtual | 2/2 | 0.0 | 0.1 | 0.4 | 0.5 | 0.080 | 15 | 93
1,000 | platform | 2/2 | 0.0 | 0.1 | 0.4 | 0.5 | 0.074 | 15 | 64
1,500 | webflux | 2/2 | 0.0 | 0.1 | 0.4 | 1.2 | 0.117 | 22 | 213
1,500 | virtual | 2/2 | 0.0 | 0.1 | 0.4 | 1.8 | 0.094 | 13 | 84
1,500 | platform | 2/2 | 0.0 | 0.1 | 0.4 | 1.3 | 0.100 | 13 | 57
2,000 | webflux | 2/2 | 0.0 | 0.1 | 0.4 | 3.7 | 0.119 | 20 | 213
2,000 | virtual | 2/2 | 0.0 | 0.1 | 0.4 | 2.7 | 0.123 | 13 | 129
2,000 | platform | 2/2 | 0.0 | 0.1 | 0.4 | 2.2 | 0.123 | 14 | 96
No database, no upstream — the control. All 24 cells valid, no errors at any rate. Nothing separates the three builds, which is what makes the other workloads readable.
Medians of the valid repetitions. valid = repetitions where k6 sustained the offered rate; ⚠ marks cells where neither did, shown greyed and not safe to quote. Latency ms, MB/1k = allocation per 1,000 requests, live MB = live set.

## Slide 19
APPENDIX · ALL CELLS
/db — every cell
rate | build | valid | err % | p50 | p95 | p99 | cores | MB/1k | live MB
500 | webflux | 2/2 | 0.0 | 0.8 | 1.0 | 1.3 | 0.193 | 61 | 81
500 | virtual | 2/2 | 0.0 | 0.6 | 0.9 | 1.0 | 0.168 | 29 | 0
500 | platform | 2/2 | 0.0 | 0.6 | 0.9 | 1.0 | 0.148 | 19 | 0
1,000 | webflux | 2/2 | 0.0 | 0.5 | 1.1 | 6.0 | 0.215 | 61 | 81
1,000 | virtual | 2/2 | 0.0 | 0.4 | 0.8 | 2.5 | 0.148 | 27 | 0
1,000 | platform | 2/2 | 0.0 | 0.4 | 0.8 | 2.0 | 0.094 | 24 | 0
1,500 | webflux | 2/2 | 0.0 | 0.5 | 1.1 | 4.1 | 0.292 | 62 | 81
1,500 | virtual | 2/2 | 0.0 | 0.4 | 0.9 | 4.4 | 0.174 | 27 | 0
1,500 | platform | 2/2 | 0.0 | 0.4 | 0.8 | 2.8 | 0.128 | 22 | 0
2,000 | webflux | 2/2 | 0.0 | 0.5 | 1.4 | 10.6 | 0.352 | 62 | 81
2,000 | virtual | 2/2 | 0.0 | 0.5 | 1.0 | 4.1 | 0.287 | 26 | 0
2,000 | platform | 2/2 | 0.0 | 0.4 | 1.1 | 4.8 | 0.157 | 23 | 0
A sub-millisecond query. All 24 cells valid, no errors. Reactive's p99 is already 2.6x the others at 2,000 rps. The live set reads 0 for both MVC builds because no old-gen collection ever ran — absent, not zero.
Medians of the valid repetitions. valid = repetitions where k6 sustained the offered rate; ⚠ marks cells where neither did, shown greyed and not safe to quote. Latency ms, MB/1k = allocation per 1,000 requests, live MB = live set.

## Slide 20
APPENDIX · ALL CELLS
/db-heavy — every cell
rate | build | valid | err % | p50 | p95 | p99 | cores | MB/1k | live MB
500 | webflux | 2/2 | 0.0 | 13.0 | 13.5 | 15.4 | 0.258 | 250 | 213
500 | virtual | 2/2 | 0.0 | 12.8 | 13.1 | 13.4 | 0.192 | 70 | 87
500 | platform | 2/2 | 0.0 | 12.8 | 13.1 | 13.4 | 0.131 | 70 | 48
1,000 | webflux | 2/2 | 0.0 | 12.7 | 15.9 | 229.3 | 0.409 | 254 | 213
1,000 | virtual | 2/2 | 0.0 | 12.4 | 12.8 | 16.8 | 0.154 | 66 | 71
1,000 | platform | 2/2 | 0.0 | 12.4 | 12.8 | 14.9 | 0.148 | 61 | 48
1,500 | webflux | 2/2 | 0.0 | 12.9 | 313.0 | 409.3 | 0.613 | 254 | 213
1,500 | virtual | 2/2 | 0.0 | 12.5 | 19.7 | 33.2 | 0.233 | 66 | 71
1,500 | platform | 2/2 | 0.0 | 12.4 | 14.8 | 28.7 | 0.211 | 64 | 48
2,000 | webflux | 0/2 ⚠ | 59.8 | 919.8 | 1,534.0 | 2,213.9 | 0.498 | 287 | 213
2,000 | virtual | 1/2 | 91.5 | 999.1 | 1,011.5 | 1,058.3 | 1.279 | 101 | 801
2,000 | platform | 2/2 | 100.0 | 1,000.2 | 1,008.1 | 1,026.8 | 0.400 | 81 | 187
The decisive workload. The tail opens at 1,000 rps, not 1,500: WebFlux's p99 is 229 ms there while its p50 is untouched. 2,000 rps is past the pool's 1,670 rps ceiling, so all three fail and WebFlux's cell is invalid on top of that.
Medians of the valid repetitions. valid = repetitions where k6 sustained the offered rate; ⚠ marks cells where neither did, shown greyed and not safe to quote. Latency ms, MB/1k = allocation per 1,000 requests, live MB = live set.

## Slide 21
APPENDIX · ALL CELLS
/api — every cell
rate | build | valid | err % | p50 | p95 | p99 | cores | MB/1k | live MB
500 | webflux | 2/2 | 0.0 | 200.9 | 201.2 | 201.3 | 0.169 | 35 | 213
500 | virtual | 2/2 | 0.0 | 200.9 | 201.2 | 214.5 | 0.268 | 56 | 144
500 | platform | 2/2 | 0.0 | 200.9 | 201.2 | 201.4 | 0.248 | 49 | 56
1,000 | webflux | 2/2 | 0.0 | 200.6 | 201.0 | 208.3 | 0.256 | 38 | 213
1,000 | virtual | 2/2 | 0.0 | 200.6 | 201.2 | 205.5 | 0.301 | 58 | 87
1,000 | platform | 2/2 | 0.0 | 668.0 | 828.7 | 858.4 | 0.241 | 56 | 69
1,500 | webflux | 2/2 | 0.0 | 200.5 | 201.0 | 205.2 | 0.310 | 39 | 213
1,500 | virtual | 2/2 | 0.0 | 200.6 | 201.3 | 207.8 | 0.397 | 59 | 147
1,500 | platform | 2/2 | 100.0 | 1,000.0 | 1,001.0 | 1,010.2 | 0.315 | 73 | 320
2,000 | webflux | 2/2 | 0.0 | 200.5 | 201.2 | 211.8 | 0.356 | 37 | 213
2,000 | virtual | 2/2 | 0.0 | 200.6 | 212.2 | 256.9 | 0.560 | 59 | 268
2,000 | platform | 0/2 ⚠ | 100.0 | 709.7 | 1,202.9 | 1,486.6 | 0.326 | 73 | 228
200 ms upstream, no database. The two candidates are indistinguishable on latency across a fourfold rate range; virtual threads pay 36 % more CPU at 2,000 rps for it. Platform threads hit Tomcat's wall exactly where Little's Law puts it: 200 / 0.2 s = 1,000 rps.
Medians of the valid repetitions. valid = repetitions where k6 sustained the offered rate; ⚠ marks cells where neither did, shown greyed and not safe to quote. Latency ms, MB/1k = allocation per 1,000 requests, live MB = live set.

## Slide 22
APPENDIX · ALL CELLS
/db-slow — every cell
rate | build | valid | err % | p50 | p95 | p99 | cores | MB/1k | live MB
500 | webflux | 2/2 | 100.0 | 712.5 | 1,000.9 | 1,001.0 | 0.430 | 790 | 203
500 | virtual | 2/2 | 99.1 | 1,000.1 | 1,000.9 | 1,013.0 | 0.296 | 121 | 717
500 | platform | 2/2 | 100.0 | 165.6 | 1,000.8 | 1,001.0 | 0.057 | 42 | 216
1,000 | webflux | 2/2 | 99.1 | 772.9 | 1,000.5 | 1,000.9 | 0.846 | 766 | 157
1,000 | virtual | 2/2 | 99.0 | 1,000.2 | 1,001.0 | 1,015.1 | 1.127 | 159 | 905
1,000 | platform | 0/2 ⚠ | 100.0 | 0.0 | 1,127.1 | 1,435.6 | 0.053 | 44 | 179
1,500 | webflux | 2/2 | 100.0 | 906.5 | 1,000.1 | 1,000.9 | 1.632 | 776 | 236
1,500 | virtual | 2/2 | 98.9 | 539.1 | 1,001.1 | 1,019.1 | 1.172 | 177 | 907
1,500 | platform | 0/2 ⚠ | 100.0 | 0.0 | 1,272.4 | 1,932.5 | 0.054 | 43 | 227
2,000 | webflux | 0/2 ⚠ | 98.0 | 729.1 | 2,167.5 | 3,354.6 | 0.144 | 599 | 213
2,000 | virtual | 0/2 ⚠ | 99.3 | 553.6 | 1,165.1 | 1,634.2 | 1.193 | 190 | 866
2,000 | platform | 0/2 ⚠ | 100.0 | 0.0 | 1,224.6 | 2,296.7 | 0.050 | 39 | 248
Every cell fails by construction — the ladder starts at 500 rps against a 200 rps ceiling. What it shows is three failure styles: platform threads refuse work at 0.05 cores, virtual threads saturate the heap, reactive burns 1.6 cores making garbage.
Medians of the valid repetitions. valid = repetitions where k6 sustained the offered rate; ⚠ marks cells where neither did, shown greyed and not safe to quote. Latency ms, MB/1k = allocation per 1,000 requests, live MB = live set.